## Slide 1: IOT (Paintball) Sight
Students: Rafi Taub (taubrafi@gmail.com)
Nick Kuhlik (nick.kuhlik@gmail.com)
Supervisor: Moni Orbach
LAB: HSDSL EE Technion
Semester: Spring 2016-5776
Notes: Nick

## Slide 2
The modern assault rifle sights is an optical device that is lacking in features.
The relay of tactical information in the field, back to the high command is mostly done by speech over the radio.
By integrating smart IOT devices into the gear of the modern infantry, we can transmit back vital data which can help in decision making.
Motivation
Notes: Nick

## Slide 3: Goals
Create a device which integrates seamlessly into standard battle gear.
Provide meaningful information to the command chain.
Self contained, fool proof.
  No burden on the user
Lightweight and low power.
  Battery life of at least 24 hours
Notes: Nick

## Slide 4: Block Diagram: Overview
GPS and MEMS data from each
Algorithm on the AWS cloud
HMI
Data creation
Collection and analysis
Decision making
Notes: Nick

## Slide 5: The cloud architecture
Server provider
AWS cloud
Server OS
Ubuntu
HTTP server
Apache
Web application
Written in python and js using Django and google maps api
Notes: Nick
Next is Rafi

## Slide 6: Block Diagram: Embedded Device
CC3200 MCU
Internet access: Wi-Fi
MEMS: orientation in space
GPS: location in space
Fired shot detection
SD storage
Barometer: relative altitude
Notes: Rafi

## Slide 7: Embedded software: key components
Shot fired detection
Read & process sensor data: GPS, accelerometer, magnetometer and barometer
Calculate orientation angles (roll, pitch, heading)
Unique hardware ID
Wi-Fi and connection to server
Hibernation & wakeup (power saving)
Notes: Rafi

## Slide 8: Interesting issues: magnetism
In a nutshell our project is strapping a magnetometer to a large piece of metal.
Materials exist in four possible categories:
  Ferromagnetic: Ni, Fe, Steel
  Paramagnetic: Sn, Al, Mg
  Diamagnetic: Cu, Pb, Brass
  Anti-Ferromagnetic: Cr
Each category affects magnetic fields in different ways.
Notes: Rafi
Ni=Nickel, Fe=Iron, Sn=Tin, Al=Aluminum, Mg=Magnesium, Cu=Copper, Pb=Lead, Cr=Chromium

## Slide 9: יהי

## Slide 10: Ideally…

## Slide 11: Problem 1 - Hard iron
Magnetized Ferromagnetic materials will offset readings in a given direction.
These offsets are independent of the orientation with respect to earth.

## Slide 12: Problem 1 - Hard iron

## Slide 13: Problem 2 - Soft iron
Paramagnetic and diamagnetic materials attract and repel the earth’s magnetic field by creating their own internal fields
The effect changes with orientation with respect to the earth.
This results in a ‘scaling’ of the proper readings.

## Slide 14: Problem 2 - Soft iron

## Slide 15: Problem 3 - Both

## Slide 16: Solution

## Slide 17: Solution
Whenever we collect a data point we compare these values with the max and min values stored for each axis.
The center of the ellipsoid is therefore:
And its axis lengths are:

## Slide 18: Solution
With this information we can define the transform:
This brings the ellipsoid to be centered about the origin and scales it to transform it back to a sphere.
We can now use this data to calculate the device’s heading.

## Slide 19: Orientation mathematics
Accelerometer data:
Corrected compass data:
roll
pitch
yaw

## Slide 20: There’s always more math
Notes: Rafi

## Slide 21: Results: PCB Design
Designed in Eagle, four layer PCB

## Slide 22: Results: Enclosure design
Designed in solidworks, 3d printed in PLA
There are better options than 3d printing

## Slide 23: Results: Enclosure
Notes: Rafi

## Slide 24: Results: The cloud
Site is located at http://52.50.107.126/ using AWS cloud.
Code is located at https://github.com/sudo-Whateverman/IOTsights

## Slide 25: Tests
Sensors: GPS, accelerometer, magnetometer, barometer.
  Nearly entirely based on the manufacturer and we need to only ‘confirm’ their results.
Battery life
Trigger testing

## Slide 26: Sensor test results
Magnetometer derived angle:
  Tested by measuring against a protractor
Accelerometer derived angle:
  Tested by measuring against a protractor
GPS location: 10m radius
  Purely dependent on GPS
Trigger sensitivity: currently set to trigger on a 5g pulse along the axis of the weapon
  Would need to be tuned to the weapon
Notes: Rafi

## Slide 27: Power consumption
Intended battery: lithium, size
3 power modes:
  Deep sleep (cold GPS): ~18 days (30sec to lock)
  Awake (warm GPS): ~5 days (3sec to lock)
  Fully active (hot GPS): ~2 days. (instant lock)
  Theoretical lifespans were 24, 8 and 5 days. (China?)
One of these options is selected at compile time.
  Could be implemented to draw settings from the server on a per unit basis.
Higher capacity batteries are available.
Notes: Rafi

## Slide 28: Demo!
http://52.50.107.126/shots/

## Slide 29: What else?
Additions:
  Encryption
  Cell network interface
  SDIO Camera
Extensions:
  Accessible Bus and UART allows addition of nearly any sensor.
  Many such devices could form a mesh network for large scale embedded sensing applications such as weather stations, agricultural monitoring, autonomous robot control, etc.
  IOT gateway for controlling any device.
Notes: Rafi

## Slide 30: Project expansion: scalability
The AWS platform gives the means to configure the deployment of several virtual machines automaticaly.
  Aws is monitoring the cpu usage/bandwith/disk usage.
  When a certain threshold that was set up is passed the group is expanded.
  When the threshold is passed on the way down, the group is shrinked and a machine is deactivated.
This creates a solution that responds quickly to abrupt surges in usage.
Notes: Nick

## Slide 31: Project expansion: bootimage over internet
In order to succesfully update the software over internet we must implement:
  Bootimage scratch space in RAM.
  Checksum of the image for validation.
  Secure transmit of the data to deter reverse engineering.
Thus we shall be able to create a decentralized solution that is future proof and shall be easily upgraded in the future.
Notes: Nick

## Slide 32: Thank you!
Special thanks to Mony, for his assistance, advice and feedback.

## Slide 33: About those Li-ion batteries…